## Slide 1: Opportunities and uncertainties in the Critical Mineral Value Chain
Rishabh Jain
India International Centre, New Delhi
28 August 2023
© Council on Energy, Environment and Water, 2023

## Slide 2: Impacting sustainable development at scale with data, integrated analysis, and strategic outreach
250+
Multidisciplinary team
380+
Peer-reviewed publications
190+
Instances of increased data transparency
540+
Roundtables & conferences
20+
Indian states engaged
130+
Bilateral & multilateral initiatives promoted
Emerging Economies
CEEW Centre for Energy Finance
UP State Office
Energy Transitions
Industrial Sustainability
Sustainable Livelihoods
Low-carbon Economy
Power Markets
TRANSFORMATIONS
QUALITY OF LIFE
Clean Air
Sustainable Mobility
Sustainable Water
Sustainable Food Systems
Sustainable Cooling
SPECIAL INITIATIVES
Powering Livelihoods
Climate Resilience
Sustainable Finance
Technology Futures
Circular Economy
ENABLERS
International Cooperation

## Slide 3: Minerals are formed from various elements and each of them have unique characteristics
Source: Ministry of Mines (2023) Image source: American Chemical Society

## Slide 4: Minerals with high supply and vulnerability risks are often categorised as Critical Minerals
Source:
Critical minerals
(High-vulnerability, high supply risk)
Non-Critical minerals
(Low-vulnerability, high supply risk)
Non-Critical minerals
(Low-vulnerability, low supply risk)
Non-Critical minerals
(High-vulnerability, low supply risk)
Vulnerability/ economic importance
Supply risk

## Slide 5: Multiple indicators can be used to calculate the mineral criticality index
Source: CEEW
Mineral criticality
Economic importance
National resource endowment
Geopolitical risk
Supply risks
Substitution risk
Recyclability risk
Industrial structure
Consumption pattern
Sectoral contribution to GDP
Sectoral mineral consumption
Import dependence
World governance index
Substitutability
Recycling potential

## Slide 6: In 2016, CEEW had identified 49 minerals important for India
Source: CEEW analysis

## Slide 7: In June 2023, MoM released the list of 30 minerals critical to India
Source: Ministry of Mines (2023) Image source: American Chemical Society
S. No. | India’s critical mineral list
1 | Antimony
2 | Beryllium
3 | Bismuth
4 | Cadmium
5 | Cobalt
6 | Copper
7 | Gallium
8 | Germanium
9 | Graphite
10 | Hafnium
11 | Indium
12 | Lithium
13 | Molybdenum
14 | Niobium
15 | Nickel
16 | Platinum group elements (6)
17 | Phosphorous
18 | Potash
19 | Rare earth elements (17)
20 | Rhenium
21 | Selenium
22 | Silicon
23 | Strontium
24 | Tantalum
25 | Tellurium
26 | Tin
27 | Titanium
28 | Tungsten
29 | Vanadium
30 | Zircon

## Slide 8: Critical minerals find use across sectors and the supply chain is distinct for each
Source: Ministry of Mines (2023)

## Slide 9: Multiple pathways can lead us to meeting our 2070 Net-Zero targets
Source: CEEW analysis

## Slide 10: The market share of various technological variants can vary significantly in the future
Note: PERC: Passivated emitter rear contact, SHJ: Silicon heterojunction, CIGS: copper indium gallium selenide; DD: direct drive, PM: permanent magnet, EE: electrically excited, SG: synchronous generator, GB: gearbox, DFIG: doubly fed induction generator; NMC: nickel manganese cobalt oxide, LFP: lithium ferro-phosphate, LMO: lithium manganese oxide, LTO: Lithium titanate oxide, PEM: proton exchange membrane
Clean energy technology -> | Solar PV | Wind | Battery | Motors | Electrolyser
 | PERC (c-Si) | DD-EESG | High-nickel NMC | Permanent magnet | Alkaline
 | SHJ | DD-PMSG | Low-nickel NMC | Induction | PEM
Important technology variants -> | CIGS (thin film) | GB-PMSG | LFP |  | Solid-oxide
 | Silicon tandem cell | GB-DFIG | LMO-LTO |  | 
 |  |  | sodium-ion |  | 
 |  |  | vanadium flow |  | 

## Slide 11: Each technology variant can have varied share of minerals and materials
 | Solar PV | Wind | EV (motor) | Battery (EV and stationary) | Electrolyser | Grid
 | Antimony | Bauxite (aluminium) | Boron | Bauxite (aluminium) | Nickel | Bauxite (aluminium)
 | Bauxite (aluminium) | Boron | Copper | Cobalt | Platinum | Copper
 | Copper | Chromium | Heavy rare earths | Copper |  | Iron (steel)
 | Gallium | Copper | Iron | Graphite |  | 
 | Indium | Heavy rare earths | Light rare earths | Iron |  | 
 | Nickel | Iron (steel) | Neodymium | Lithium |  | 
 | Selenium | Light rare earths |  | Manganese |  | 
 | Silicon | Manganese |  | Nickel |  | 
 | Silver | Molybdenum |  | Vanadium |  | 
 | Zinc | Neodymium |  | Zinc |  | 
 | Tin | Nickel |  | Phosphorus |  | 
 | Iron (steel) | Zinc |  | Fluorine |  | 

## Slide 12: The market share of technological variant will determine the total mineral demand
Source: EU JRC (2020), Fraunhofer ISE (2022)
 | Solar module material intensity (kg/MW) |  |  | 
Select technology variants -> | PERC | SHJ | CIGS | Tandem
Copper | 869 | 922 | 90 | 574
Silicon | 3038 | 2934 |  | 2362
Indium |  |  | 108 | 15
Gallium |  |  | 26 | 52
 | Wind turbine material intensity (kg/MW) |  |  | 
Select technology variants -> | DD-EESG | DD-PMSG | GB-PMSG | GB-DFIG
Copper | 5000 | 3000 | 950 | 1400
Rare earths | 44 | 239 | 62 | 14
Nickel | 340 | 240 | 440 | 430
Molybdenum | 109 | 109 | 119 | 99

## Slide 13: Upcoming and disruptive technologies can reduce the critical mineral demand
Source: EU JRC (2020), Fraunhofer ISE (2022)
 | Battery material intensity (kg/MWh) |  |  |  | 
Select technology variants -> | Lithium ion (LFP-G) | Lithium ion (NMC532-G) | Lithium-ion (NMC811-G) | Vanadium flow | Sodium-ion*
Lithium | 96 | 126 | 93 |  | 
Nickel |  | 522 | 614 |  | 
Cobalt |  | 210 | 77 |  | 
Phosphorus | 427 | 12 | 11 |  | 
Copper | 466 | 311 | 284 | 220 | 
Graphite | 1055 | 879 | 915 | 530 | 
Vanadium |  |  |  | 5185 | 

## Slide 14: 15 countries are home to at least 55 per cent of each of the identified critical minerals
Source: CEEW Analysis from USGS, 2023

## Slide 15: A handful of countries make up more than 70 per cent of the mine production of all of the identified critical minerals
Source: CEEW Analysis from USGS, 2023

## Slide 16: Upstream and midstream manufacturing processes are concentrated in few regions
Source: IEA (2021)

## Slide 17: The upstream and midstream value chain will create new opportunities - Solar
17|
Source: ISA (2023)

## Slide 18: The upstream and midstream value chain will create new opportunities - Wind
18|

## Slide 19: The upstream and midstream value chain will create new opportunities – LiB batteries
Anode active material manufacturing
Electrolyte manufacturing
Cell manufacturing
Battery assembly
Lithium-ion cell
Lithium-ion battery
Cathode active material manufacturing
Separator
manufacturing
Consumable
Compounds of lithium, cobalt, nickel, manganese, iron and/or aluminium
Consumable
Graphite (synthetic/natural), silicon or LTO
Consumable
LiPF6
Organic solvents
Consumable
Polymer (polyolefin)
Other consumable
Current collector foils (copper and aluminium), cell casing, binder, solvent
Other consumable
Casing, connectors, battery management system hardware, communications bus

## Slide 20: How can India tap the upcoming opportunity
India will need to find more mineral resources to meet domestic and international demand. Exploration will be the key now.
For the existing mineral resources, timely and sustainable mining will be crucial so that import dependence can be reduced. New mining technologies need to be developed to increase mineral recovery but reduce impact on nearly ecology.
Indigenisation of mineral processing and raw material manufacturing will be important to increase the domestic value add of the mineral supply chain
India can leverage being the fastest growing economy and recover minerals from various products when they reach end of life
International collaboration & cooperation can speed up efforts and India should leverage the geopolitical sentiment of diversification

## Slide 21
Thank you
ceew.in | @CEEWIndia